Hexapod notes

PWM Driver Board = PCA9685 PWM control
-Adafruit documentation: https://learn.adafruit.com/16-channel-pwm-servo-driver?view=all
        Overview: https://www.adafruit.com/product/815

-need for an added capacitor ?
-install Adafruit PWMServo library: https://github.com/adafruit/Adafruit-PWM-Servo-Driver-Library
-Adafruit class documentation: https://circuitpython.readthedocs.io/projects/pca9685/en/latest/api.html
-test arduino code: https://learn.adafruit.com/pages/643/elements/848850/download
#include <Wire.h>
1. #include <Adafruit_PWMServoDriver.h>
3. Adafruit_PWMServoDriver pwm1 = Adafruit_PWMServoDriver(0x40);
4. Adafruit_PWMServoDriver pwm2 = Adafruit_PWMServoDriver(0x41);
6. void setup() {
7. Serial.begin(9600);
8. Serial.println("16 channel PWM test!");
10. pwm1.begin();
11. pwm1.setPWMFreq(1600); // This is the maximum PWM frequency
13. pwm2.begin();
14. pwm2.setPWMFreq(1600); // This is the maximum PWM frequency
15. }

Servos:
- operating voltage: 4.8 to 7.2 Volts
- running current: 500 mA - 900 mA (6V)
- stall current 2.5A (6V)
- dead band width: 5 us
- max stall torque = 11 kg/cm at 6 V
- metal gear, dual ball bearing
- can rotate 60 degrees in either direction - 120 degree total travel
- data sheet shows example with 50 Hz frequency, 20 ms period
- wire 1 = Brown = ground
- wire 2 = Red = Motor power , usually +5V
- wire 3 = Orange = PWM signal
- draws 2.5A at 6 V
- stall torque = 9.4 kg/cm at 4.8V
- speed = 0.17 sec/60 degrees
- motor weight = 55 gm
- specs: https://components101.com/motors/mg996r-servo-motor-datasheet
- data sheet: https://components101.com/asset/sites/default/files/component_datasheet/MG996R-Datasheet.pdf
- PWM board library: http://adafruit.github.io/Adafruit-PWM-Servo-Driver-Library/html/class_adafruit___p_w_m_servo_driver.html#ac725dd6b0d24d087586a854e81bcf6b3
- info on booting/downloading and need for pushing boot buttons
    https://github.com/espressif/esptool/wiki/ESP32-Boot-Mode-Selection

To Do
- test 30 pin devkit using Andrew’s code
- survey ESP32 and ESP8266 inventory
    - ignoring 8266’s
    - 2 * 30 pin DEVKIT-V1
    - 2 * 36 pin DEVKIT-V1 (new pins: CMD, SD3, SD2, CLK, SD0, SD1, D0) (lost pin: 1 GND)

- build master spreadsheet for CPU comparison, notably pins