Task: Given the location of the toe at point T = (Tx, Ty, Tz), find the servo rotation angles for the hip Rh, knee Rk and ankle Ra with angles expressed in degrees.

Approach: Find the coordinates of the ankle (Ax, Ay, Az) and from there calculate the angles.

Finding the hip angle is straight forward. Looking down from above, the leg’s projection in the xz plane is a straight line that is the hypotenuse of a right angled triangle with the X axis, with the hip angle between these 2 lines. Therefore:
   tan(Rh) = Tz/Tx, or Rh = arctan(Tz/Tx) // spreadsheet uses ATAN2(x,y) function

Based on this, we can use Rh in calculating the ankle coordinates.

To reduce the 3D problem to 2D, envision rotating the hip servo so its angle is zero, and the leg is sticking straight sideways.

Viewing from the top again, we have a plane that’s like (x,y) coordinates but in our case is (x,z) with the x axis going outward from the center of the robot, and the z axis going forward.

The formula for rotating a 2D vector (x,y) through a counter clockwise angle T is:
   (x,y) --> ( x*cos(T) - y*sin(T) , x*sin(T) + y*cos(T) )

to apply this to the path of the toe in our case, we have to:
- account for our angle being clockwise
- account for our different coordinates

if (Ux, Uy, Uz) represents the rotated position of the toe, then:
   Ux = Tx * cos(-Rh) - Tz * sin(-Rh) // from x coordinate of 2D vector rotation formula
   Uy = Ty // our rotation doesn’t change the y coordinate of any points
   Uz = 0 // we selected our rotation to give this

Now let’s look at the plane where z = 0, containing our rotated leg sticking straight out sideways.

The ankle lies on a circle of radius 7.5 cm, centred on the knee which is 2.5 cm from the origin,
       above the hip servo, at y=0.
It also lies on a circle with radius 11 cm, centred on the toe, at (Ux, Uy, Uz)

The formula for a circle is ( x - Xc)^2 + (y - Yc)^2 = r^2
  where (Xc,Yc) is the center, and r is the radius

The equation for the first circle is:
     (x - 2.5)^2 + (y - 0)^2 = 7.5^2
     x^2 -5*x + y^2 = 50 (1)

for the second circle:
    (x - Ux)^2 + (y - Uy)^2 = 11^2
    x^2 -2*x*Ux + Ux^2 + y^2 -2*y*Uy + Uy^2 = 121 (2) (y - Uy)^2 = 121 - (x - Ux)^2, y = +/- sqrt( 121 - (x - Ux)^2 ) + Uy

subtracting equation (2) from equation (1)...
-5*x + 2*Ux*x - Ux^2 + 2*Uy*y - Uy^2 = 50 - 121

rearranging...
x*(-5 + 2*Ux) + y*(2*Uy) = 50 - 121 + Ux^2 + Uy^2

y = ( -71 + Ux^2 + Uy^2) - x*(-5 + 2*Ux) (3)
      ----------------------------------------------
        2 * Uy

substituting y as defined by (3) back into equation (1)

x^2 - 5*x + ( (-71 +Ux^2 + Uy^2) -x*(-5 + 2*Ux) )^2 - 50 = 0
        -------------------------------------------------
        (2 * Uy)^2

x^2 - 5*x + (-71 +Ux^2 + Uy^2)^2 - 2*((-71 + Ux^2 + Uy^2) * x *(-5 + 2*Ux)) + ((-5 + 2*Ux)*x)^2 - 50 = 0
        ------------------------------------------------------------------------------------------------------------
        4* Uy^2

x^2 - 5*x + (-71 + Ux^2 + Uy^2)^2 - 2*((-71 + Ux^2 + Uy^2)*-5*x - 2*((-71 + Ux^2 + Uy^2)*2*Ux)*x) + ((-5 + 2*Ux)*x)^2 - 50 = 0
        ----------------------------------------------------------------------------------------------------------------------------------------------
        4* Uy^2

x^2 - 5*x + (-71+Ux^2+Uy^2)^2 - 2*(-71+Ux^2+Uy^2)*-5*x - 2*((-71+Ux^2+Uy^2)*2*Ux)*x) + 25*x^2 - 20*Ux*x^2 + 4*Ux^2*x^2 - 50 = 0
        ----------------------------------------------------------------------------------------------------------------------------------------------------------
        4* Uy^2

x^2*( 1 + 25 -20*Ux+4*Ux^2) + x *( -5 + -2*(-71+Ux^2+Uy^2)*-5 - 2*((-71+Ux^2 + Uy^2)*2*Ux) + (-71+Ux^2+Uy^2)^2 - 50 = 0
        -------------------------- ------------------------------- -------------------------------------- --------------------------
        4 * Uy^2 4 * Uy^2 4 * Uy^2 4 * Uy^2

which is a quadratic equation in x, with solutions ( - b +/- SQRT( b*b - 4*a* c) / (2 * a)

a = 1 + ( 25 - 20*Ux + 4*Ux^2 ) / ( 4 * Uy^2)

b = -5 + ( -2 * (-71 +Ux^2 + Uy^2) *-5 + -2*( ( -71 + Ux^2 + Uy^2) * 2 * Ux) ) / (4 * Uy^2 )

c = (-71 + Ux^2 + Uy^2) ^2 / (4 * Uy^2 ) -50

By observation, we want the + choice of the +/- in the quadratic formula if Ty <0, otherwise -ve. If Ty >0, the math that calculates Ra messes up, but I’m working on it.

Let a program or spreadsheet do the math, and calculate x. Substitute it into equation (1) or (3) to get y.
Rk = arctan(x / y) Ra = arctan((Ux - x) / (Uy - y)) - 17 degrees < these have been revised several times, and are still changing.

        .........................................................................................................